## Slide 1
Force control in hydraulic cylinders
with variable impedance
Genova, Italy – November 2015
Job Ledezma
Claudio Semini
Victor Barasuol
Supervisors:
PhD Student:

## Slide 2
Introduction
Pure Hydroelastic Actuator
Chronogram
Structure of
this presentation
1
2
5
Hydraulic Actuator with Variable Impedance
3
Control technique
4

## Slide 3
Introduction
Introduction
1

## Slide 4
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram
Florianópolis is the capital city and second largest city of the state of Santa Catarina, in the South of Brazil. It is composed of one main island, a continental part and the surrounding small islands.
The city is known for having a very high quality of life, ranked as the country's third highest Human Development Index score among all Brazilian cities.

## Slide 5
The Federal University of Santa Catarina (UFSC) is a public university in Florianópolis, the capital city of Santa Catarina. It is one of the leading Brazilian and Latin American research universities, mainly noted for its engineering school.
It campus is divided in 11 Educational Centers, which are divided in departments. The largest one is the Department of Mechanical Engineering. The oldest is the Center of Juridic Sciences, that is itself the department of Law, which was the first of UFSC's departments to be officially recognized in 1932.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 6
LASHIP – Laboratory of Hydraulic and Pneumatic Systems of the Department of Mechanical Engineering at the Federal University of Santa Catarina has a structure focused on attending university activities of education, research and services.
The LASHIP’s team is involved with undergraduate education since 1977 and graduate education and research on hydraulic and pneumatic components and systems since 1984.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 7
1 – Analysis and Design of Hydraulic and Pneumatic Systems and Components;
2 – Integration of Hydraulics and Pneumatics with software and electronics: Mechatronic Solutions;
3 – Computational systems to support the design of hydraulic systems and components
Research areas:
The research funds are from government projects and partnerships with industries. Besides the infrastructure in equipment and facilities, it is established a group made by 3 professors and about 15 people among research engineers and graduate and undergraduate students connected through institutional projects and industry.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 8
Position and force control are the most common types of hydraulic systems control. However, besides the similarities between them, force control is analytically more complex than position control because the dynamics of the environment has to be included in the control system design.
>>
Force
Control
Position
Control
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 9
Hydraulic actuation systems are very stiff due to low compressibility of the fluid and, consequently, very small movements of the cylinder can generate large force variations when the hydraulic actuator is in direct contact with the environment.
Incrementing the system compliance through the reduction of the transmission stiffness would overcome this intrinsic problem of force control.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 10
The compliance in actuators can be obtained by two ways:
Active
Passive
software
hardware
Force feedback-based
Usually expensive due to the high precision process hardware required for this work.
Doesn’t store energy.
Fast change of apparent stiffness.
Mechanical components
insertion
Usually cheaper.
Store energy.
It’s possible to vary the stiffness but requires a more sophisticated hardware (not fast)
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 11
Plummer (2007)
Lamming et al. (2010)
Sivaselvan et al. (2008)
A spring is a passive element that stores energy and limits the force rate applied over the load or environment. Consequently, it produces a filter effect that increases the system compliance and contributes to obtaining good performances.
The use of springs decrease the complexity of the mathematical model.
Incrementing passively the compliance of the system
Increments the stability during the force control
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 12
The Hydro-elastic Actuator uses a linear hydraulic actuator followed by a spring where the applied force is indirectly calculated from the measure of the spring deflection.
Hydro-SEA has good force stability, low output impedance, and tolerance to shock loading. However, it shows bandwidth reduction when large forces are applied at power saturations limits
The most referenced actuator in the literature using a passive compliance method for controlling the force is the Series Elastic Actuator (SEA) proposed by Williamson (1995). Robinson (2000) extend this study to hydraulic systems and proposed the Hydro-elastic Actuator.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 13
Remote manipulator proposed by Buerguer (2005).
Hydroelastic actuator proposed by Robinson (2000).
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 14
Pure Hydroelastic Actuator
Pure Hydroelastic Actuator
2

## Slide 15
The main focus in this case is to show the possibility to obtain hydraulically the same behavior obtained by the SEA, extracting the spring and using High Volumetric Expansion (HVE) Hoses or Accumulators.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 16
Pure HydroElastic Actuator
PHEA
This actuation system reduces the hydraulic stiffness using only hydraulic components. Additionally, it saves space in the axial direction and allows a direct contact between the actuator and environment.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 17
The selection of the hydraulic components is based on the principle that the fluid in the cylinder chambers presents a spring effect that can be modulated by adding hydraulic capacitive components, such as high volumetric expansion hoses (HVE hoses) or accumulators.
K
CC
K
H
Hydraulic Stiffness
s
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 18
Hydraulic System
Continuity equation
Rod movement equation
Movement equation
Cylinder
Servovalve
Environment
Flow-rate dynamics
Spool movement equation
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 19
SERVOVALVE MODELLING
Spool movement equation:
Flow-rate dynamics:
for UC ≥ 0 (xsp ≥ 0):
for UC < 0 (xsp < 0):
Introduction
Mathematical modelling
Analysis and Selection of Compliant Components
Application example
Conclusions

## Slide 20
CYLINDER MODELLING
Continuity equation:
Rod movement equation:
Force applied:
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 21
For low stiffness reductions, HVE hoses may be selected. Such hoses allow a bigger hydraulic capacitance compared to the common hoses.
The hydraulic stiffness varies nonlinearly with respect to the piston position (xp):
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 22
Assuming that the entrance of air into the system is almost nonexistent such that have no influence on the performance of the system, the effective bulk modulus is directly modified by the variation of the container bulk modulus (be ≈ bC = bhose).
Finally, the required hose length can be calculated:
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 23
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 24
Hydraulic Actuator with Variable Impedance
Hydraulic Actuator with Variable Impedance
3

## Slide 25
Hydraulic actuator versatile enough to maintain the system stability despite any variation of the environment stiffness.
Actuator capable of self modify its hydroelasticity in a controlled way fulfilling tasks of force and position control.
Hydraulic Actuator with Variable Impedance
HAVI
PHEA
Dynamic
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 26
System with a complex hardware;
Higher economical cost;
It’s necessary to develop a new kind of hydraulic component with variable capacitance;
If necessary, a variable damping component should be added, too.
Compact and hydraulically pure system;
Hydraulic actuator that actually doesn’t exist.
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 27
Control technique
Control technique
4

## Slide 28
Was created by the Prof. Isaac Horowitz (1959). It’s a linear technique that adds quantitative characteristic in the frequency analysis initially proposed by Bode (1945).
Quantitative management
Model uncertainties
Disturbances
Plant model
+
Uncertainties
Performance requirements
Bounds
Loopshaping
Performance
Robustness
F
G
+
QFT
Quantitative Feedback Theory
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 29
Based on a 2-DOF canonical system:
Reference
Disturbance before the plant
Disturbance after the plant
Controller
Prefilter
Plant
Sensor
Output
Noise
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 30
QFT
Procedure
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 31
Design and experimental evaluation of a robust force controller for an electro-hydraulic actuator via quantitative feedback theory.
Niksefat & Sepehri (2000)
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 32
Chronogram
Chronogram
5

## Slide 33
Implement the PHEA in the FC1D;
Experimental validation;
Implement the PHEA in the HyL;
Propose and obtain simulation responses of the HAVI;
Implement the HAVI in the FC1D.
Experimental validation.
Tasks | Months |  |  |  |  |  | 
 | 1° | 2º | 3º | 4º | 5º | 6º | 7º
1 |  |  |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
Introduction
Pure Hydroelastic Actuator
Hydraulic Actuator with Variable Impedance
Control Technique
Chronogram

## Slide 34
?
?
?
?
Thanks !
Any questions ??

## Slide 35
www.laship.ufsc.br/fpni2016